Application

MXB Coarse Powder Mill is a kind of new high-tech

milling machine to meet the requirements of coarse

powder   processing   customers.   Based   on   our

experts' years' research experience in the milling

industry  and  considering  recommendations  and

requirements of domestic and foreign clients. It is

the ideal equipment to replace Raymond Mill, ball

mill, and other traditional mill which only process

fine   powder   materials.   It   is   high-efficiency

equipment and widely applied in quartz sand, silica

sand,  foundry  sand,  fine  sand  and  other  sand

abrasive industry. By being a component of closed

production   lines,   it   can   produce   various   size

products of better effect.

Working Principle

Step with main shaft, bulk disk and roller bracket is

driven by motor through reducer. Installed above

bracket,  roller  assembly  rotates  with  main  shaft

and  swings  freely  meantime,  this  bring  a  large

centrifugal  force,  which  scatters  bulk  materials

evenly  in  grinding  intermediate  layer  between

central  roller  and  ring.  The  bulk  materials  are

grinded into powder and fall on the bottom, and

then  discharged  from  discharging  opening  under

the effect of synchronously-rotating scraper.

Technology Advantages

High efficiency of wear material, wear evenly, the

lifetime is three times higher than that of Raymond

Mill;

High percentage of sand can be produced by this

machine;

The   mill   is   a   highly   efficient   desulfurization

equipment of power plant. It can grind CaCO3 into

fine powder less than 1-2mm, the desulfurization

effect is better;

This machine can be used as pre-grind equipment

before ball mill; the ball mill efficiency will increase

50%;

Products out of this machine can be used to make

firebrick,  concrete  brick,  block  and  other  new

building materials;

Mainly used for pre-processing of various crushable

non-inflammable  &  non-explosive  brittle  material

with Mohs Hardness less than nine.

Specification

Name/Parameter/Product

Model

MSB1004

4

<30

70-90%<2

8-15

37-45

1870x1500x2580

8

Roller quantity(pcs)

Max. feeding size(mm)

Product size(mm)

Capacity(ton/hour)

Main motor power(kw)

Overall size(mm)(LxWxH)

Total weight (excluding electricity control cabinet)(ton)

MSB1205

5

<35

70-90%<2

16-30

75-90

2350x1850x2850

14

Jaw crusher

Power(kw)

Bucket elevator

Power(kw)

Vibrating feeder

Power(kw)

Optional Equipment

PE(X)150x750

15

TH250

3

GZ3F

0.2

PE(X)250x1000

30

TH315

7.5

GZ4F

0.4

Note: This specification is just reference, any changes are subject to products.

SHANGHAI SHIBANG MACHINERY CO., LTD.

Website: http://www.quarrycrusher.com

E-mail: sbm@unisbm.com         Postcode: 201201

Office Add: 416th, Jianye Rd., Pudong New District, Shanghai, China