What we do today is to ensure the future of our

group with youth and spirit forever and ever.

- SBM

The most professional

Impact Crusher in China

After introducing advanced techniques, SBM impact crushers

is optimized and widely applied in the first and secondary

crushing. It can crush material like granite, basalt, bluestone,

etc the longest side of which is less than 500mm, and

anti-pressure strength is not more than 320Mpa, and the final

product is ideal device for aggregation used in highway and

railway surface as well as water and electricity industry.

SBM Impact Crusher Overview

Impact crushers are suitable for materials whose co

mpressive strength is under 360Mpa, and particle size is

under 500mm. This kind of machine features easy

maintenance, high crushing ratio and crushing efficiency etc.

With end products in cubic shape, impact crushers are the

ideal crusher for aggregates processing in high-type highway

building, water conservancy and power construction.

They are suitable for materials whose compressive strength

is under 360Mpa and side length is under 500mm. They are

preferred to crush granite, limestone, rivel gravel, etc.

World-class craftsmanship and materials

Impact crusher Main Features and Benefits

1. Energy-efficient.

2. Unique structure, keyless connection.

World-class design

3. Blow bar made of high chromium steel, impact plate with a special shape.

4. End products with cubical shape.

5. Easy operation and maintenance and high reliability.

Impact crusher Technical Data

Type

Spec.

PF-1010    1000�1050

PF-1210    1250�1050

PF-1214    1250�1400

PF-1315    1320�1500

Feeder

Opening(mm)

400�1080

400�1080

400�1430

860�1520

Feeding

Size

(mm)

350

350

350

500

Crushing

Motor

Weight(t)

Capacity(t/h)    Power(KW)

50-80

70-120

130-180

160-250

55-75

110-132

132-160

180-260

12

14

18.6

19

How Impact Crusher works

It   uses   plate   hammer   on   the   rapidly

rotating   rotor   to   generate   high-speed

impact   to   crush   the   materials   in   the

crushing  cavity,  and  casts  the  crushed

materials   along   tangential  direction   to

impact  plate  at   the  other  end   of  the

crushing    cavity.    The    materials    are

crushed  again,  and  then,  they  return  to

the plate hammer to undergo the process

above   repeatedly.   The   materials   are

bumping  with   each   other  when   being

sent between  the plate hammer and  the

impact   plate.   The   materials   become

cracked, loose  and  then  comminuted  by

knocking  by  the  plate  hammer,  impact

with   impact   plate  and   bump  between

materials.  The  materials  with  grain  size

smaller  than  the  gap  between   impact

plate  and  plate  hammer  will  be  disch-

arged.

Sales Hot-Line

International Dept.1: Tel: 0086-21-58383098

International Dept.2: Tel: 0086-21-58383028

International Dept.3: Tel: 0086-21-58383058

International Dept.4: Tel: 0086-21-58383003

International Dept.5: Tel: 0086-21-58383022

E-mail & Fax

E-mail:

Fax:

sbm@unisbm.com

0086-21-58383058

Office Address & Zip

Add : No.416 Jianye Road,South Jinqiao Area,Pudong, Shanghai, China

Zip / Postal Code : 201201