VSI5X series VSI rock crusher:

VSI5X series VSI rock crusher (sand making machine) brief introduction:

SBM VSI5X series VSI rock crusher (sales code: VSI5X) is a new generation high effective product

which introduces  German technology, and owns many  independent patents  property. The VSI

rock crusher integrates three crushing methods into one. All of these made it the core equipment

in sand making industries.

VSI5X series VSI rock crusher (sand making machine) is suitable for:

VSI5X  series  VSI  rock  crusher  is  widely  used  in  metal  and  nonmetal  mine,  cement,  concrete,

fireproof   material,  abrasive  filler,   glass  raw   materials,   frit,  construction  aggregate,  sand,

metallurgy and so on.   It is also applicable to crush various stones with different hardness in

medium and fine crushing area, such as iron ore, non ferrous metal, emery, bauxite, quartz sand,

pearlite, basalt, etc.

VSI5X series VSI rock crusher (sand making machine) features and benefits:

1)   Rotor with deep chamber increases 30% capacity after perfect design.

2)   Side plate direction can be changed to increase material utility ratio, operating ratio can be

increased 48%.

3)   Worn hammer with combined type is only changed to reduce operating cost 30%. Another

pair of vice hammer is added to prevent from damaging main hammer and side plate.

4)   The  most  key  wear  resistant  material  uses  wear  resistant  and  high  temperature  resistant

material in American important area.

5)   Rhombus shape impact plate is used to prevent side plate from being damaged.

6)   Bearing is famous international brand imported from Japan, Sweden, America, etc.

7)   Perfect discharge and smooth curve reduce resisting force when material flows, so capacity is

increased greatly.

8)   Spread dish with double purposes can make two feeding ways change easily.

9)   Special seal structure under main shaft guarantee no oil leak without seal.

10) Japanese hydraulic opening cover device is originally imported. The cover is moved easily and

inspection of inner part is easy.

11) Motor with high grade of protection is selected. The motor has features of high efficiency,

low noise, etc. The motor complies with IEC, insulation grade F, protection grade IP54/55.

VSI5X series VSI rock crusher working principle:

Feed at center:

Materials fall into the hopper and then through the feeding opening in the center enter the high

speed  rotor  which  will throw out  the  materials with  high  speed.  Materials  firstly strike  those

materials that are free falling down.. Then, materials strike the materials-liner in the vortex or the

impact liner and are rebounded to the top of crushing chamber and then fall down. After that,

the falling materials with materials shot from the impeller form a continuous materials curtain.

Ultimately, crushed materials will be charged from the discharging opening.

Feed both in the center and from sides:

The materials fall into the hopper and the circle hole and then will be divided into two parts by

the distributing plate. One part of materials cross the distributing plate and enter the high speed

impeller and then is accelerated and thrown out .The other part falls down from the sides of

distributor.  Materials  firstly  strike  the  free  falling  down  materials.  Then,  materials  strike  the

materials-liner in the vortex or the impact liner and are rebounded to the top of crushing cavity

and then fall down. The falling materials with materials shot from the impeller form a continuous

curtain of materials. At last, crushed materials will be discharged from the discharging opening.

VSI5X series VSI rock crusher specification:

Model

Throughput

capacity(t/h)

Max feed size

(mm)

Feed both at

center and sides

Feed

soft

materials

Hard materials

rotation speed(r/min)

Double motor power (kw)

Overall dimension L*W*H (mm)

weight(t)

Power supply

Power of double

lubropump

motor

Light-oil

lubrication

station

safety

protection

Oil-tank heating

power

Overall

dimension

L*W*H (mm)

VSI5X7615

150~280

70~140

<35

<30

1700~1900

110~150

3700�2200

�2300

8.6

VSI5X8522

240~380

120~200

<40

<35

1500~1700

180~220

4140�2300

�2700

11.8

VSI5X9532

350~540

180~280

<45

<40

1300~1510

260~320

4560�2500

�2900

17.5

VSI5X1145

500~640

250~360

<50

<45

1100~1310

400~440

5000�2700

�3400

27.5

380v，50Hz

2X0.31kW

Double complementary lubropumps supply oil. Auto-stop without

oil flow. Water-cool system. Motor-heating for winter.

2kW

820X520X1270

VSI5X series VSI rock crusher image:

Contact E-mail: sbmglobal@gmail.com

Address:

No.416 Jianye Road,South Jinqiao Area,Pudong New Area

Shanghai, China

Zip:

201201

Sales Hotline:

INTERNATIONAL TRADE DEPT.1: Tel: 0086-21-58383022 Fax:0086-21-58383058

INTERNATIONAL TRADE DEPT.2: Tel: 0086-21-58383058 Fax:0086-21-58383058

INTERNATIONAL TRADE DEPT.3: Tel: 0086-21-58383003 Fax:0086-21-58383058

INTERNATIONAL TRADE DEPT.4: Tel: 0086-21-58383098 Fax:0086-21-58383058